## Slide 1: MRI ARTIFACTS

## Slide 2: What are artifacts?
Artifacts are simply signal misrepresentations that do not correspond to the location of the specific tissue imaged.

## Slide 3: What causes artifacts?
The Patient/ Subject
Magnetic Field Inhomogeneity
Machine Hardware

## Slide 4: Motion artifact
seen as a smearing across an image.
Primarily caused from patient/subject voluntary movement
Can be caused by involuntary movement such as:
  Oesophageal contraction/ vascular pulsation during head and neck imaging
  Respiration/ cardiac activity during T-spine/Abdominal imaging
  Bowel peristalsis during pelvic imaging

## Slide 5: MAGNETIC SUSCEPTABILITY
Artifacts resulting from the presence of metallic objects.
Distorts nearby structures & causes signal loss

## Slide 6: Aliasing/ wrap around artifact
Occurs when tissue outside the field of view is under sampled, causing misregistration of anatomic location.
Easily identified by the superimposition/incorrect location of anatomy

## Slide 7: Zipper artifact
A Leak in the RF shielding
Can appear due to inadequate door suction in the MR scan room.